## Slide 1: EEGScaler: A Network to scale EEG electrodes and samples for MI Speed Decoding
Praveen K Parashiva, Sagila K Gangadharan and A. P. Vinod

## Slide 2: Motivation
Decoding kinematics information such as speed and direction from imagined hand movement results in a more natural control of BCI.
Challenges:
  EEG offers poor spatial resolution
  For decoding speed, the spatial overlap between two actions (fast and slow) is large.
Objective: Propose a deep learning based method to decode MI actions imagined at two speed – fast and slow.

## Slide 3: Dataset
14 Subjects (7M and 7F, Age: 30.9
33 electrodes (F3, F1, Fz, F2, F4, FC5, FC1, FCz, FC2, FC4, FC6, C5, C3, C1, Cz, C2, C4, C6, CP5, CP3, CP1, CPz, CP2, CP4, CP6 )
actiCHamp, Brain Products
Sampling frequency 500 Hz
Analysis Window: 12 sec to 17 sec
Preprocessing:
Baseline Removal : 1sec cue data is baseline
CAR
Bandpass filtering : 0.1 to 90 Hz, 5th order butterworth
Notch filter : IIR filter with Q-factor 20

## Slide 4: Proposed Method : Electrode Scaling
A

## Slide 5: Proposed Method : Sample Scaling
B

## Slide 6
EEG Trial (33 x 2000)
Conv2D : 1 x 64 Kernel, padding, filters = 8 Output: 8 x 33 x 2000
Electrode-Scaling Block
Sample-Scaling Block
A
B
A
B
Batch Normalization
Conv2D : 33 x 1 Kernel, padding, filters = 16 Output: 16 x 1 x 2000
Batch Normalization
Exponential Linear Unit Activation
A
B
B
Average Pooling (size = 8)
Dropout
Conv2D : 1x16 kernel, padding = same, bias = False Output: 16 x 1 x 500
Batch Normalization
Exponential Linear Unit Activation
Average Pooling (size = 8)
Dropout
Flatten Layer
Dense Layer
SoftMax
Proposed Method

## Slide 7
A)
B)

## Slide 8: Results
SubID | SMC 2024 [1] | Proposed Method
S01 | 54.17 | 54
S02 | 52.08 | 56.22
S03 | 64.58 | 62.66
S04 | 60.42 | 68.88
S05 | 66.67 | 58.88
S06 | 58.33 | 60.66
S07 | 52.08 | 64.66
S08 | 56.25 | 73.55
S09 | 58.33 | 58.88
S10 | 60.42 | 65.11
S11 | 68.75 | 52.44
S12 | 60.42 | 71.11
S13 | 54.17 | 60
S14 | 66.67 | 56.88
Average | 59.52428571 | 61.70928571
[1] Sagila and A. P. Vinod, “Decoding Speed and Direction of Imagined Hand Movement from EEG-BCI”, IEEE SMC October 2024, Malaysia

## Slide 9
Average Pooling
Fully Connected Layer
B)

## Slide 10
a)
b)
c)

## Slide 12
Chart: 
| S01 | S02 | S03 | S04 | S05 | S06 | S07 | S08 | S09 | S10 | S11 | S12 | S13 | S14
 | 54.17 | 52.08 | 64.58 | 60.42 | 66.67 | 58.33 | 52.08 | 56.25 | 58.33 | 60.42 | 68.75 | 60.42 | 54.17 | 66.67
 | 71.1111 | 86 | 72.8889 | 73.1111 | 75.1111 | 65.1111 | 55.1111 | 69.3333 | 58.2222 | 56.8889 | 62.8889 | 52.2222 | 62.4444 | 65.1111
 | 66.8889 | 69.1111 | 73.3333 | 62.6667 | 68.6667 | 62.2222 | 46 | 78 | 56 | 56.4444 | 67.1111 | 69.1111 | 68.8889 | 52.4444
 | 56 | 67.3333 | 79.1111 | 74.8889 | 73.5556 | 79.5556 | 54.2222 | 75.3333 | 56.2222 | 58.2222 | 54.8889 | 70.6667 | 48.2222 | 75.5556

## Slide 13
Chart: 
| S01 | S02 | S03 | S04 | S05 | S06 | S07 | S08 | S09 | S10 | S11 | S12 | S13 | S14
 | 50 | 52.08 | 54.17 | 50 | 50 | 50 | 58.33 | 54.17 | 62.5 | 52.08 | 50 | 39.58 | 52.08 | 45.83
 | 54.17 | 52.08 | 64.58 | 60.42 | 66.67 | 58.33 | 52.08 | 56.25 | 58.33 | 60.42 | 68.75 | 60.42 | 54.17 | 66.67
 | 71.1111 | 86 | 72.8889 | 73.1111 | 75.1111 | 65.1111 | 55.1111 | 69.3333 | 58.2222 | 56.8889 | 62.8889 | 52.2222 | 62.4444 | 65.1111
 | 66.8889 | 69.1111 | 73.3333 | 62.6667 | 68.6667 | 62.2222 | 46 | 78 | 56 | 56.4444 | 67.1111 | 69.1111 | 68.8889 | 52.4444
 | 56 | 67.3333 | 79.1111 | 74.8889 | 73.5556 | 79.5556 | 54.2222 | 75.3333 | 56.2222 | 58.2222 | 54.8889 | 70.6667 | 48.2222 | 75.5556
Subject ID
Cross-Validated Classification Accuracy (%)
EEGNet [3]
W-CSP and MRSP [10]
Sample-Scaling Only
Both Electrode and Sample Scaling
Electrode-Scaling Only